A710GRB,A710GRB Steel Plate,A710GRB Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting A710/A710M A710GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Precipitation-Strengthened Low-Carbon Nickel-copper-Chromium-Molybdenum-Columbium Alloy Structural Steel Plates, Which is a large steel plate supplier mill at Gangsteel Group. A710GRB,A710/A710M A710GRB,A710GRB Steel Plate,A710GRB HIC,A710GRB Nace

Tags: A710GRB,A710/A710M A710GRB,A710GRB Steel Plate,A710GRB steel factory, A710GRB adopt standard, A710GRB Heat treatment, A710GRB Technical delivery condition, A710GRB Chemical, A710GRB Mechanical property, A710GRB Price, A710GRB CEV, A710GRB Impact degree, A710GRB impact energy, A710GRB Supplier,A710GRB Specification, A710GRB properties, Material A710GRB N, A710GRB Material, A710/A710M, A710GRB Steel, A710GRB Yield, A710GRB plate, A710GRB HIC, A710GRB NACE MR0175, A710GRB ISO 15156, A710GRB NACE MR0103, A710GRB SSC

Keyword: A710GRB,A710GRB Steel Plate,A710GRB Supplier

1.  A710GRB Adopt standard: ASMT A710/A710M Standard Specification for Precipitation-Strengthened Low-Carbon Nickel-copper-Chromium-Molybdenum-Columbium Alloy Structural Steel Plates.

2.  A710GRB Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A710GRB: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A710GRB Chemical composition % of the Product analysis of grade

| Grade | C % | Mn % | P% | S% | Si% | Ni% |
| --- | --- | --- | --- | --- | --- | --- |
| A710GRB | 0.03-0.09 | 0.45-1.3 | 0.025 | 0.025 | 0.3-0.5 | 0.8-1.0 |
|  | Mo% | Cu% | Cb% | Ti% | Cr% |  |
|  | 0.25 | 1.25-1.5 | 0.05-0.06 | 0.01-0.03 | 0.3 |  |

5.  A710GRB Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A710GRB | 485Mpa | 550Mpa | <6.5mm | 20% |
|  | 485Mpa | 550Mpa | 6.5-8mm | 20% |
|  | 485Mpa | 550Mpa | 8-10mm | 20% |
|  | 485Mpa | 550Mpa | 10-12.5mm | 20% |
|  | 485Mpa | 550Mpa | 12.5-20mm | 20% |
|  | 485Mpa | 550Mpa | 20-25mm | 20% |
|  | --- | --- | 25-30mm | 20% |
|  | --- | --- | 30-50mm | 20% |
|  | --- | --- | 50-100mm | -- |
|  | --- | --- | >100mm | -- |

6.  Normally A710/A710M A710GRB plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A710GRB Delivery Time Or Lead Time: 20-35days

8.  A710GRB Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A710GRB, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting A710/A710MA710GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A710GRB,A710/A710M A710GRB,A710GRB Steel Plate,A710GRB HIC,A710GRB Nace

Tags: A710GRB,A710/A710M A710GRB,A710GRB Steel Plate,A710GRB steel factory, A710GRB adopt standard, A710GRB Heat treatment, A710GRB Technical delivery condition, A710GRB Chemical, A710GRB Mechanical property, A710GRB Price, A710GRB CEV, A710GRB Impact degree, A710GRB impact energy, A710GRB Supplier,A710GRB Specification, A710GRB properties, Material A710GRB N, A710GRB Material, A710/A710M, A710GRB Steel, A710GRB Yield, A710GRB plate, A710GRB HIC, A710GRB NACE MR0175, A710GRB ISO 15156, A710GRB NACE MR0103, A710GRB SSC